## Slide 1: Computer Architecture
Week 3

## Slide 2: Objectives
Representing negative numbers using two’s complement
Computer components as building blocks
  Subtraction based on addition
  Bit shifter
To introduce the concept of an ALU

## Slide 3: Computer Components
CPU: Central Processing Unit
  The part of the computer that carries out instructions
  Different makes of CPU will have different instructions they can do
Considered to contain
  ALU: arithmetic/logic unit
  Control unit

## Slide 4: ALU
Different computer processor families will have different operations available and could include:
  Arithmetic operations (add, subtract, multiply)
  Bitwise AND, OR, NOT etc
  Shift all the bits in an input
  Compare inputs

## Slide 5: Joining Instructions
Join at vevox.app
Or search Vevox in the app store
ID: 165-289-715

## Slide 6: What is the result of a bitwise AND between 1001 and 1110?
Join: vevox.app ID: 165-289-715
Enter Text and Press Send
Vote Trigger
The correct answer is
1000
79.03% of participants answered correctly

## Slide 7: ALU: common features
The ALU takes two operands (A and B)
  Binary signals to carry out an operation on
There is an input Opcode
  A code for which operation is needed
The output is the result of carrying out the required operation on A and B
There may be output status / condition code indicators
Often all the available instructions will be done at the same time (in parallel) and the relevant result selected to pass to the output
Image credit: By Lambtron - Own work, CC BY-SA 4.0,
https://commons.wikimedia.org/w/index.php?curid=36975996

## Slide 8: What component can we use to select one from a number of inputs?
Join: vevox.app ID: 165-289-715
POLL OPEN
Vote Trigger
ü
1
Decoder
5.81%
2
Multiplexer
81.4%
3
Comparator
11.63%
4
Ripple-carry adder
1.16%

## Slide 9: ALU from last year’s coursework
Pins show hexadecimal values
One task was to amend the ALU so that operation 3 multiplies the two inputs.

## Slide 10: Amended ALU from last year’s coursework

## Slide 11: Performance considerations
What a computer can do depends on hardware and software combined
How many functions should an ALU have?
  For example, you can code multiplication as repeated addition so don’t need to include multiplication in an ALU
  Putting multiplication in the ALU would make it more complex and expensive to create the hardware, but programs that need a lot of multiplication would run faster.

## Slide 12: Binary numbers
We have seen how to represent positive integers in binary format
For example, binary 1100110
In decimal is 64 + 32 + 4 + 2 = 102
128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
0 | 1 | 1 | 0 | 0 | 1 | 1 | 0

## Slide 13: Representing negative numbers
There are several different ways that have been proposed to represent negative numbers, we will cover the one that is almost universal in modern computers, two’s complement
  If we just had one bit for the sign (+ or -)
    We would end up with two different representations of zero
    We would need more complex circuits for addition
Using two’s complement
  Addition works as you would expect for positive and negative numbers

## Slide 14: What do you get if you do a bitwise NOT operation on 00001101?
Join: vevox.app ID: 165-289-715
Enter Text and Press Send
Vote Trigger
The correct answer is
11110010
94.29% of participants answered correctly

## Slide 15: Binary addition
Adding 1
00010101
+ 00000001
==========
00010110

## Slide 16: What do we get if we add 1 to the binary number 0100?
Give your answer as four bits
Join: vevox.app ID: 165-289-715
Enter Text and Press Send
Vote Trigger
The correct answer is
0101
85.9% of participants answered correctly

## Slide 17: Two’s complement
To get the two’s complement of a binary number
  Invert each of the bits
  Add 1 to the result (binary addition)

## Slide 18: What is the 8-bit two’s complement of the binary number 00011011?
To get the two’s complement of a binary number
Invert each of the bits
Add 1 to the result
Give an 8-bit answer
Join: vevox.app ID: 165-289-715
Enter Text and Press Send
Vote Trigger
The correct answer is
11100101
88.31% of participants answered correctly

## Slide 19: Two’s complement to represent negatives
To express a decimal value in two’s complement binary:
If the number is positive (or zero)
  Convert it to binary in the normal way
  There needs to be at least one leading zero
If the number is negative:
  Work out the binary of the positive value
  Take the two’s complement of that binary number

## Slide 20: Two’s complement
The number of bits being used for the representation is important
When the most significant bit is one, the number is negative
  11101010 is negative
  01101101 is positive
For 8-bit representation, two’s complement is equivalent to using the column headings
-128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
0 | 1 | 1 | 0 | 0 | 1 | 1 | 0

## Slide 21: Which of the following 8-bit two’s complement numbers are negative?
You do not need to convert the numbers to decimal for this task.
Join: vevox.app ID: 165-289-715
POLL OPEN
Vote Trigger
Vote for up to 2 choices
(% = Percentage of Voters)
ü
ü
1
00101011
2.74%
2
10110010
87.67%
3
00011111
4.11%
4
10001001
95.89%

## Slide 22: Two’s complement example
To get the binary for -27 in 8-bit two’s complement
  Work out the binary for +27
  Invert all the bits
  Add 1 to give the representation for -27
00011011
11100100
11100101

## Slide 23: Two’s complement exercise
To get the binary for -5 in 8-bit two’s complement
  Work out the binary for +5
  Take the two’s complement
00000101

## Slide 24: What is the 8-bit two’s complement of the binary number 00000101?
To get the two’s complement of a binary number
Invert each of the bits
Add 1 to the result
Give an 8-bit answer
Join: vevox.app ID: 165-289-715
Enter Text and Press Send
Vote Trigger
The correct answer is
11111011
81.82% of participants answered correctly

## Slide 25: Two’s complement exercise
To get the binary for -5 in 8-bit two’s complement
  Work out the binary for +5
  Invert all the bits
  Add 1 to give the representation for -5
00000101
11111010
11111011

## Slide 26: Two’s complement – binary to decimal
To get the decimal equivalent of 11110010 which represents a number in 8-bit two’s complement
The most significant bit is a 1, so we know it’s a negative number
  Take the two’s complement then convert to decimal and add a minus sign
  Flip all bits
  Add 1
  Convert 1110 to decimal
    Is 8 + 4 + 2
    gives 14
The original number 11110010 was -14
00001101
00001110

## Slide 27: Two’s complement – binary to decimal – alternative approach
To get the decimal equivalent of 11110010 which represents a number in 8-bit two’s complement
Alternative approach – change the column heading for the rightmost bit to be negative
Convert to decimal as normal by adding up the column headings where a 1 appears
  -128 + 64 + 32 +16 + 2
The original number 11110010 was -14
-128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
1 | 1 | 1 | 1 | 0 | 0 | 1 | 0

## Slide 28: Using online tools
For this unit, you need to be aware of two’s complement but can use any online tools to do the conversion

## Slide 29: Two’s complement - range
Using 4-bit representation
  All possible binary values are 0000 … 1111
  Remember that gives us 16 different values
All numbers starting with 1 are negative
All the positive numbers we can make are
  000 to 111 (that is 0 to 7 in decimal)
All the negative numbers we can make are
  1000 to 1111 (-8 to -1 respectively in decimal)
We have 16 different values from decimal -8 to +7
  Note that if we add 1 to 111 (decimal 7) we get 1000 (decimal -8)

## Slide 30: Subtraction by adding a negative
Suppose we want to work out the decimal calculation 48 - 19
We can treat it as 48 + (-19)
We have seen that we can create a component for addition and can use a gate to invert a value
This might be easier or cheaper than building a separate component for subtraction

## Slide 31: Subtraction by adding a negative: 48 + (-19)
Using 8-bit two’s complement
  48 is binary 00110000
  +19 is binary 00010011
Two’s complement of 00010011
  Invert gives 11101100
  Add 1 11101101
Add the two numbers and ignore the overflow:
  00110000
  11101101 +
  ---------
  00011101
Convert back to decimal to check
  Binary 11101 is decimal 29

## Slide 32: Summary
The ALU is a component that can carry out multiple operations on two inputs. The opcode determines which result will be output.
Two’s complement is the most common way to represent negative numbers in binary
In next week’s lab
  We will look at further components – decoder and bit shifter
  We will build an ALU in Logisim Evolution