## Slide 1: Computer Architecture
Week 9

## Slide 2: Objectives
Continue to look at control transfer instructions
  Unconditional control transfer
    Subroutines using jal and ret
  Conditional control transfer
    Branch statements

## Slide 3: Jump instructions
We have seen how to use
jal to jump to the code following a label (set the pc to the address of that code) and store the address of the instruction after the jal in register ra
ret to set the program counter back to the address stored in ra

## Slide 4: Branching
Allows conditional changes in execution path
  Then we can code if/else type statements and loops
Based on some condition we either continue on the code path or move to a different part of the program
There are many different variations of branch instructions in RISC-V basic and pseudo-instructions. We will only look at a few of them.

## Slide 5: Example branch instructions in RISC-V
Conditional basic instructions
  Go directly to the instruction after the label if register1 is not equal to register2
    bne, register1, register2, label
  Go directly to the instruction after the label if register1 is greater than or equal to register2
    bge, register1, register2, label
  Go directly to the instruction after the label if register1 is less than register2
    blt, register1, register2, label
Unconditional branch (pseudo instruction)
  Go directly to the instruction after the label
  b label
Notes: Note there are many more

## Slide 6: Pass or fail?
Suppose we want the user to input their mark and the program will tell them if it’s a pass or a fail
  Get the user input into a register
  Assume that the user inputs an integer in the correct range (0 to 100)
  Compare the mark to 40
    Store 40 in a register (I’ll use t0)
    Multiple ways to approach this
  If the mark is greater than or equal to 40
    It is a pass
  Otherwise,
    It is a fail

## Slide 7: Pass or fail? Approach 1
Check if the grade is greater than or equal to 40
Using branch greater than or equal to bge
  If the input result is greater than or equal to 40 then branch to code for a pass
  Otherwise, when the branch wasn’t followed it is a fail
    In that case make sure to skip the code for a pass using branch (b)

## Slide 8: Pass or fail – 1
.data
msgPass: .string "You passed, well done"
msgFail: .string "You failed this time"
.text
addi a7, zero, 5
ecall
addi t0, zero, 40
bge a0, t0, pass
la a0, msgFail
b output
pass:
la a0, msgPass
output:
addi a7, zero, 4
ecall
The program will continue to the instruction after the bge when the value is not greater than 40
Receive integer input from the user and store in register a0
If a0 is greater than or equal to t0, go to pass
These lines run if we didn’t branch to pass
We need to skip the load of the pass message
Store 40 in register t0

## Slide 9: Pass or fail? Approach 2
Check if the grade is less than 40
Using branch less than blt
  Branch to code for fail if grade is less than 40
  Otherwise, when branch wasn’t followed it is a pass
  If the input result is less than 40 then branch to code for a fail
  Otherwise, when the branch wasn’t followed it is a pass
    In that case make sure to skip the code for a fail using branch (b)

## Slide 10: Pass or fail – 2
.data
msgPass: .string "You passed, well done"
msgFail: .string "You failed this time"
.text
addi a7, zero, 5
ecall
addi t0, zero, 40
blt a0, t0, fail
la a0, msgPass
b output
fail:
la a0, msgFail
output:
addi a7, zero, 4
ecall
Using blt
The program will continue to the instruction after the blt when the value is not less than 40
If a0 is less than t0 then go to fail
Store 40 in register t0
Receive integer input from the user and store in register a0
These lines run if we didn’t branch to fail

## Slide 11: Which instruction do we use to always branch without testing any condition?
bne
b
beq

## Slide 12: Checking for equality
Suppose we are trying to code a guess the number game where the computer generates a random number (say between 1 and 100) and the player has to guess it
  There are system calls available in RARS to set up a random number
We would need to provide hints as to whether the guess was too high or too low
For now we will just look at checking whether the guess was correct or not

## Slide 13: Checking for equality – using bne
Assembly tests opposite case (i != j) of high-level code (i == j)
Java Code
if (guess == secret)
// correct
else
// wrong
RISC-V assembly code
# relate registers to java code
# s0 = secret, a0 = guess
bne s0, a0, wrong
# load address of win message
# branch to continue
wrong:
# load address of lose message
continue:
# output the message

## Slide 14: Checking for equality – using beq
Java Code
if (guess == secret)
// correct
else
// wrong
RISC-V assembly code
# relate registers to java code
# s0 = secret, a0 = guess
beq s0, a0, win
# load address of lose message
b continue
win:
# load address of win message
continue:
# output the message

## Slide 15: What would this code output?
Nothing
Red Blue
Red
Blue
.data
red: .string "Red "
blue: .string "Blue "
.text
addi a7, zero, 4 # to output a string
addi t0, zero, 3
addi t1, zero, 4
bge t0, t1, choice
la a0, red
b output
choice:
la a0, blue
output:
ecall

## Slide 16: What does the code output now?
Nothing
Red Blue
Red
Blue
The code won’t run
.data
red: .string "Red "
blue: .string "Blue "
.text
addi a7, zero, 4 # to output a string
addi t0, zero, 4
addi t1, zero, 4
bge t0, t1, choice
la a0, red
b output
choice:
la a0, blue
output:
ecall

## Slide 17: Pseudo instructions
Pseudo instructions are not actual RISC-V instructions, but they are often more convenient for the programmer
Assembler converts them to real RISC-V instructions.

## Slide 18: Some pseudo instructions for conditional branching
Go directly to the instruction after the label if register1 is equal to zero
  beqz, register1, label
Go directly to the instruction after the label if register1 is not equal to zero
  bnez, register1, label
Go directly to the instruction after the label if register1 is greater than register2
  bgt, register1, register2, label
Notes: Note there are many more

## Slide 19: What does the pseudo instruction bgez stand for?
1
Branch if greater than zero
0%
2
Branch if equal to zero
0%
3
Branch if greater than or equal to zero
0%

## Slide 20: What would the pseudo instruction ble stand for?
1
Branch if less than or equal to
0%
2
Branch if less than
0%
3
Branch always
0%

## Slide 21: Creating a countdown loop
addi a0, zero, 5
addi a7, zero, 1
loop:
ecall
addi a0, a0, -1
bnez a0, loop

## Slide 22: Loops counting up – approach 1
Java Code
// add the numbers from 0 to 9
int sum = 0;
int i = 0;
int end = 10;
while (i < end) {
sum = sum + i;
i++;
}
// print out the sum
RISC-V assembly code
# s0 = i, s1 = sum
# t0 = limit for counting
# set up the initial values
addi s1, zero, 0
addi s0, zero, 0
addi t0, zero, 10
loop:
bge s0, t0, done
add s1, s1, s0
addi s0, s0, 1
b loop
done:
# print out the sum

## Slide 23: Loops counting up – approach 2
Java Code
// add the numbers from 0 to 9
int sum = 0;
int i = 0;
int end = 10;
while (i < end) {
sum = sum + i;
i++;
}
// print out the sum
RISC-V assembly code
# s0 = i, s1 = sum
# t0 = limit for counting
# set up the initial values
addi s1, zero, 0
addi s0, zero, 0
addi t0, zero, 10
loop:
add s1, s1, s0
addi s0, s0, 1
blt s0, t0, loop
# print out the sum

## Slide 24: What is the final value in s0 after the code has run?
addi s0, zero, 0
addi t0, zero, 3
loop:
addi s0, s0, 1
blt s0, t0, loop

## Slide 25: What is the final value in s0 after the code has run?
addi s0, zero, 0
addi t0, zero, 3
loop:
addi s0, s0, 1
ble s0, t0, loop
Notes: Answer s0 will have 4

## Slide 26: What is the final value in s0 after the code has run?
addi s0, zero, 0
addi t0, zero, 3
loop:
addi s0, s0, 1
bge s0, t0, loop
Join: vevox.app ID: 159-043-242

## Slide 27: Beware infinite loops
Because we are using an emulator (RARS) we can use the stop button to stop a program that is stuck in an infinite loop
addi s0, zero, 0
addi t0, zero, 3
loop:
addi s0, s0, 3
bge s0, t0, loop

## Slide 28: Summary
Standard programming constructs of if/else and loops are all implemented using branch instructions